## Slide 1: Pocket DAQ manual
Mar. 10, 2016
Satoru Yamada

## Slide 2
COPPER III
HSLB
HSLB
HSLB
HSLB
COPPER
CPU
Network
switch
Readout
PC (PXE boot server)
FEE
FEE
FEE
FEE
Ethernet
B2link
Connection between components (COPPER-II/III)
TTRX ver.5
FTSW
VME CPU(VMIC)
About port assignment of FTSW, see
svn+ssh://xxx@bdaq.local.kek.jp/bdaq/svn/firmware/ft2u/trunk/doc/ft2u.pdf
Cat7 LAN cable
9U slots
6U slots

## Slide 3
COPPER CPU
Readout PC
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
Merger :
eb0.cc
recorder:
RecvStream1.py
Old Software components
RootOutput.root
Orange color components are basf2 components.
reader:
ReadStore.py
These are stored under https://stash.desy.de/projects/B2/repos/software/browse/daq
COPPER CPU
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py

## Slide 4
Readout PC
Merger :
eb0.cc
recorder:
RecvStream1.py
Old Software components (from rev. 13542 to rev. 15005)
RootOutput.root
Orange color components are basf2 components.
reader:
ReadStoreTemplate.py
These are stored under https://stash.desy.de/projects/B2/repos/software/browse/daq
recorder:
RecvStream0.py
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
COPPER CPU
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
recorder:
RecvStream0.py
COPPER CPU

## Slide 5
Readout PC
Merger :
eb0.cc
recorder:
RecvStream1.py
New Software components (from rev. 15006)
RootOutput.root
Orange color components are basf2 components.
reader:
ReadStoreTemplate.py
These are stored under https://stash.desy.de/projects/B2/repos/software/browse/daq
Receive/send:
RecvStream2.py
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
COPPER CPU
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
Receive/send:
RecvStream2.py
COPPER CPU

## Slide 6
If you run pocket-DAQ on readout PCs in E-hut (e.g. klm case), basically eb0 cannot be used without Konno-san’s nshm-based run-control system.
In that case, you need to bypass eb0 to use Pocket DAQ as shown in the following figure.
  You need to change some parameters in RecvStream1.py for this bypass. (next page)
Alternative scheme not w/o eb0(1)
Readout PC
recorder:
RecvStream1.py
RootOutput.root
Orange color components are basf2 components.
reader:
ReadStoreTemplate.py
Receive/send:
RecvStream2.py
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
COPPER CPU
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
Receive/send:
RecvStream2.py
COPPER CPU

## Slide 7
# Receiver
…
receiver.param('NumConn', 1)
receiver.param('HostNameFrom', ['localhost'])
receiver.param('PortFrom', [int(argvs[2]) ])
With eb0 : (default )
Without eb0 w/ one COPPER (192.168.10.102 )
Alternative scheme w/o eb0(2)
# Receiver
…
receiver.param('NumConn', 1)
receiver.param('HostNameFrom', ['localhost‘ ])
receiver.param('PortFrom', [34002] )
How to change daq/rawdata/examples/RecvStream1.py
Without eb0 w/ 3 COPPERs (192.168.10.102, 192.168.10.105, 192.168.10.110 )
# Receiver
…
receiver.param('NumConn', 3)
receiver.param('HostNameFrom', ['localhost‘, 'localhost‘, 'localhost‘ ])
receiver.param('PortFrom', [34002, 34005, 34010 ] )
Usually, 5101 is used as argvs[2].
It is a port # of eb0.
3400* is a port # of RecvStream2.py
You need to connect it directly from RecvStream1.py

## Slide 8: Pocket DAQ w/o slow controller and GUI

## Slide 9: 0. Before using pocket DAQ
Setup a PXE boot server for COPPER CPU and install driver for COPPER etc
  See https://confluence.desy.de/display/BI/DAQ+PocketDAQ
Install basf2 on both COPPER CPU and Readout PC
  See https://confluence.desy.de/display/BI/Software+SoftwareInstallation
    “addall” might not install the daq package. Then, you need to do “addpkg daq”.
  Check daq/Sconscripts and comment out “if env['CONTINUE'] = False” line.
  Compile with scons.
Compile eventbuilder
  cd ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0/ ; gmake eb0

## Slide 10: Notice from Konno-san about compiling daq package
Please run the following command to update nsm2 programs in your external directory
$ source ${BELLE2_LOCAL_DIR}/ daq/slc/extra/nsm2/export.sh
Otherwise you may get error messages about compilation of slow control programs ;
daq/slc/nsm/src/NSMData.cc: In member function 'void* Belle2::NSMData::parse(const char*, bool)':
daq/slc/nsm/src/NSMData.cc:299:68: error: too many arguments to function 'NSMparse* nsmlib_parsefile(const char*, int, const char*, char*)'
In file included from include/daq/slc/nsm/NSMData.h:20:0,
from daq/slc/nsm/src/NSMData.cc:1:
IMPORTANT!
Edit daq/rawdata/modules/include/DAQConsts.h
Comment out a nonstop DAQ releated line, which cannot be used in Pocket DAQ.
Before)
#define NONSTOP
After)
// #define NONSTOP

## Slide 11: Install GLEW for running basf2 program
After external ver.0.5.0?, basf2 requires GLEW(The OpenGL Extension Wrangler Library).
The following procedure worked fine.
1, install the yum epel repository.
ropc01$ wget http://ftp-srv2.kddilabs.jp/Linux/distributions/fedora/epel/5/i386/epel-release-5-4.noarch.rpm
(for SL6 64bit, ropc01$ wget ftp.riken.jp/Linux/fedora/epel/6/x86_64/epel-release-6-8.noarch.rpm )
ropc01$ ssh cpr** -lroot
cpr**# rpm -ivh epel-release-5-4.noarch.rpm
cpr**# ls -lrt /etc/yum.repos.d/
cpr**# exit
2, install glew on COPPER
ropc01$ sudo yum install glew --installroot=/tftpboot/copper/root

## Slide 12: 0.25, Establish belle2link
From Nakao-san’s mail : [b2link_ml:0159] Re: ft2u-0.65, b2tt-0.31, hslb-0.36
To partially mask HSLB, one can modify register 130 of tt4r:
- setting each of bit 0..3 to 0 corresponds to masking HSLB A..D
- default value of register 130 is 0010000f (all HSLB are enabled)
- bit 20..23 are read only and should be 1 as above
- for example, one can mask HSLB-A by
copper_CPU $ regrx 130 0000000e
Example :
When you use;
Slot A : copper_CPU $ regrx 130 00000001
Slot B : copper_CPU $ regrx 130 00000002
Slot A and B : copper_CPU $ regrx 130 00000003
- tesths
-- tesths tries to clear all errors (and optionally read out COPPER)
-- it tries all known reset procedure to establish the belle2link
-- can be used with no argument, "tesths -a" to establish the belle2link
-- can be used with number of events "tesths -ab -10000" to read out 10000 events.
-- it does read the copper device driver and check the Belle2link and
HSLB headers/trailers and print out some of the results, but it does not save the main data.
0.5, Set active HSLB slots in TTRX register
From “svn co svn+ssh://username@bdaq.local.kek.jp/bdaq/svn/firmware/hslb/trunk/hsprogs/README.hsprogs”

## Slide 13: 1, Set parameters in run_start.sh (1)
[ROPC] % cd ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts
[ROPC] % emacs run_start.sh
Set arguments of start_copper.sh
Usage : start_copper.sh <HOSTNAME> <COPPER node> <FINNESSE bit flag: A=1, B=2, C=4, D=8> <Use network shared memory : Yes=1, No=0> <node name(used for Network Shared Memory)>
e.g.)
/usr/bin/xterm -e ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/start_copper.sh cpr006 1 1 0 0&
/usr/bin/xterm -e ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/start_copper.sh cpr007 2 3 0 0&
<COPPER node ID> will be attached to RawCOPPER header.

## Slide 14
1, Set parameters in run_start.sh (2)
NOTICE : Environment variables for basf2
In ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/copper.sh, a line, “source ~/.bash_profile”, is for setting up basf2 environment. You need to add basf2 setting commands in your .bash_profile (or other script file).
Please see "Setup of Software Tools" at https://confluence.desy.de/display/BI/Software+SoftwareInstallation for details.
[ ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/copper.sh ]
#
# setup basf2 environment (See "Setup of Software Tools" at https://belle2.cc.kek.jp/~twiki/bin/view/Computing/SoftwareInstallation
#
source ~/.bash_profile

## Slide 15
1, Set parameters in run_start.sh (3)
Set arguments of RecvStream2.sh
Usage : RecvStream2.py <COPPER hostname> <Use NSM(Network Shared Memory)? yes=1/no=0> <port # to accept connection from eb0 > <NSM nodename>
Example :
/usr/bin/xterm -e "${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/RecvStream2.sh cpr001 0 34001 hogehoge1000;” &
/usr/bin/xterm -e "${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/RecvStream2.sh cpr007 0 34007 hogehoge1000;” &
Readout PC
Merger :
eb0.cc
RecvStream2.py
cpr001
cpr007
RecvStream2.py
Port
33000
Port
33000
Port
34001
Port
34007

## Slide 16
1, Set parameters in run_start.sh (4)
Specify whether communication with GUI via shared memory will be used or not :
1, Edit ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/RecvStream1.py
If you use GUI, set ‘UseShmFlag’ = 1
receiver.param('UseShmFlag', 1)
If you don’t use GUI set ‘UseShmFlag’ = 0
receiver.param('UseShmFlag', 0)
2, Edit ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/RecvStream2.py
If you use GUI, set ‘UseShmFlag’ = 1
receiver.param('UseShmFlag', 1)
If you don’t use GUI set ‘UseShmFlag’ = 0
receiver.param('UseShmFlag', 0)

## Slide 17: 1-1, Edit RecvStream1.py
$ emacs release/daq/rawdata/examples/RecvStream1.py
There are basf2 modules to be used in the scripts
    main.add_module(receiver) : receive data from eb0
    main.add_module(converter) : Convert RawDataBlock to RawDetector object (optional )
    main.add_module(dump) : Record received data on disk
    main.add_module(sender) : Send data downstream
For PocketDAQ purpose, receiver, converter and dump modules are basically used. So please modify the script like the following.
    main.add_module(receiver)
    main.add_module(converter)
    main.add_module(dump)
    # main.add_module(sender)

## Slide 18
2, Setting of merger (eb0) (1)
1, compile
$ cd ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0
$ make
2, edit eb0.sh
cd /home/usr/b2daq/eb # change to cd “your local BelleII directroy”/daq/eventbuilder/evb0/eb-xinetd
( e.g. cd /home/usr/yamada/basf2/release/daq/eventbuilder/evb0/eb-xinetd )
If you want to read data from COPPERs with hostnames of cpr010, cpr011 and cpr012 and corresponding port # of RecvStream2.py are 34010, 34011 and 34012, respectively, use the following ;
./eb0 cpr010:33000 cpr011:33000 cpr012:33000
./eb0 localhost:34010 localhost:34011 localhost:34012
Merger :
eb0.sh
RecvStream2.py
cpr010
cpr011
RecvStream2.py
Port
33000
Port
33000
Port
34010
Port
34011
cpr012
RecvStream2.py
Port
33000
Port
34012
Readout PC (localhost)
RecvStream1.py

## Slide 19
2, Setting of merger (eb0) (2)
3, edit eb0’s part in ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0/eb-xinted
Modify user and server.
service eb0
{ bind = 127.0.0.1
socket_type = stream
type = UNLISTED
port = 5101
wait = no
user = g0cdc # Change to your user name (e.g. yamagata)
server = /home/usr/b2daq/eb/eb0.sh
# change to “your Belle2 local directory”/daq/eventbuilder/evb0/eb0.sh
# (e.g. /home/usr/yamagata/basf2/release/daq/eventbuilder/evb0/eb0.sh)
}
You need to change the other services in eb-xinetd ( eb1tx, eb1rx, eb2tx, eb2rx …. ) in the same way.

## Slide 20
4, Set link to eb-xinetd
# cd /etc/xinetd.d/
# ln –s ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0/eb-xinetd eb-xinetd
# /sbin/service xinetd restart
The eb0 daemon will be automatically invoked when a basf2 program on a readout PC connects to a port specified in eb-xinted.
2, Setting of merger (eb0) (3)

## Slide 21: 3, How to start DAQ
[ROPC] % cd ${BELLE2_LOCAL_DIR}/release/daq/copper/daq_scripts
[ROPC] % ./run_start.sh
It is convenient to login COPPER w/o typing password.
For example;
ropc $ cd ~/.ssh
ropc S ssh-keygen rsa
ropc $ cat ./id_dsa.pub >> authorized_keys
ropc $ chmod 600 authorized_keys

## Slide 22: 4, How to stop DAQ
No stop button for now (If you use GUI, you have.)
You need to specify max # of events or time to stop the run on a basf2 python file.
ROPC % cd ${BELLE2_LOCAL_DIR}/daq/rawdata/examples
Edit RecvStream1.py
You can set following paramters to stop a run.
receiver.param('MaxTime', 300.)
receiver.param('MaxEventNum', 30.)
-1 means inifinite.

## Slide 23: 5. Read an output file and extract FEE buffer
Output file name
  ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/root_output.root
  You can change the filename by editing ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/RecvStream1.py
Read the root file
  Please see dataformat and unpacker manuals.
  Data format
    https://stash.desy.de/projects/B2/repos/software/browse/daq/copper/doc/SetupPocketDAQ_4p1_RawCOPPERDataFormat.pdf
  Unpacker
    https://stash.desy.de/projects/B2/repos/software/browse/daq/copper/doc/SetupPocketDAQ_4p5_RawDataUnpackerPacker.pdf

## Slide 24: Revision history(1)
2013/10/16
  Change explanation about option of run_start.sh script
2014/7/15 (rev. 11619)
  To specify FINESSE bit field, you need to use decimal value ( not hexadecimal ).
  Add an argument of RecvSenDCOPPER.py
  Update eb0 related issues.
    About eb0.sh
    About eb0-xinted
2014/7/16(rev. 11654)
  eb0.sh and eb-xinetd need more modification
2014/7/19
  Add a comment about “addpkg daq”
2014/8/8
  Modify usage of start_run.sh. (nodename is only used for NSM)
2014/10/29
  Change a DAQ scheme so that RecvStream0.py is used on a readout PC
2014/11/10
  Add figures to indicate connection between COPPER and FTSW
  Add procedure to ssh-login w/o typing password
2014/11/14
  Add “Notice from Konno-san about compiling daq” page
2015/1/22
  Use RecvStream2.py(=DesSerPrePC.cc) instead of RecvStream0.py(=DeSerializerPrePC.cc+Serializer.cc)

## Slide 25: Revision history(2)
2015 4/13
  Add “0.5, Set active HSLB slots in TTRX register”
2015 5/08
  Add an “Edit RecvStream1.py” page
2015/7/14
  Add an instruction to use PoecketDAQ w/o eb0.
2016/2/22
  Comment out “# define NONSTOP” in DAQConsts.h for Pocket DAQ
2016/3/10
  Add warning to use external v01-01-01.
2016/4/14
  Add tesths description from Nakao-san’s bdaq-svn README file
2017/11/27
  Combined COPPER III setup page with COPPER II’s
  Modify old svd/cc.kek.jp links to desy’s.

## Slide 26: Appendix

## Slide 27: A-1, yum setting for COPPER
Sometime yum fails when you try to install software to COPPER directory;
readoutPC # yum install **** --installroot=/tftpboot/copper/root
In that case, you need to change yum setting for COPPER host:
1, Copy yum repository files. readoutPC # cp /etc/yum.repo.d/* /tftpboot/copper/root/etc/yum.repo.d/*
2, Set a proxy server in /tftpboot/copper/root/etc/yum.conf same as readoutPC:/etc/yum.conf

## Slide 28: A-2, Socket parameters on COPPER, readout PC and etc..
1, Enable “Jumbo Frame” in network switch’s setting, if necessary (e.g. HP1810-24G)
If the switch does not support Jumbo frame, setting MTU a large value may cause a problem.
2, Change socket parameters
# /sbin/ifconfig eth? mtu 9000
# /sbin/sysctl -w net.ipv4.tcp_rmem="8388608 8388608 8388608"
# /sbin/sysctl -w net.ipv4.tcp_wmem="8388608 8388608 8388608"
# /sbin/sysctl -w net.ipv4.tcp_mem="9000000 9000000 9000000"
# /sbin/sysctl -w net.core.rmem_default=8388608
# /sbin/sysctl -w net.core.wmem_default=8388608
# /sbin/sysctl -w net.core.rmem_max=8388608
# /sbin/sysctl -w net.core.wmem_max=8388608
3, edit /etc/rc.local(or /tftpboot/copper/root/etc/rc.local ) if you want the parameters automatically set at boot time

## Slide 29
A-3, Use ntpd to adjust time on COPPER
1, Edit /tftpboot/copper/root/etc/rc.d/init.d/ntpd
# Source networking configuration.
. /etc/sysconfig/network
ntpdate 192.168.10.1
if [ -f /etc/sysconfig/ntpd ];then
. /etc/sysconfig/ntpd
fi
2, check ntpd is started at boot time
cpr**** $ chkconfig –list | grep ntp

## Slide 30: A-4, syslogd
Install syslogd :
readoutPC # yum install syslogd --installroot=/tftpboot/copper/root
Add entry to /tftpboot/copper/root/etc/syslogd.conf if needed:
# Log anything (except mail) of level info or higher.
# Don't log private authentication messages!
*.info;mail.none;news.none;authpriv.none;cron.none /var/log/messages

## Slide 31
Read Out PC
CDC test board
(Ver.3)
COPPER
FTSW
TTD
GbE
Belle2link
Clock+
Trigger
B-1, Test bench at Tsukuba B3