## Slide 1
How to setup “ROPC(SL6 64bit)/COPPER(SL5 32bit)” system
from the current“ROPC(SL5 32bit)/COPPER(SL5 32bit)”
S. Yamada (KEK)
Dec. 10, 2016

## Slide 2
1. Setup environment
Archive tftpboot directory and other files on the old ROPC.
  [Old ROPC: / ] $ tar cvf ~/tftpboot.tar /tftpboot
  Copy /etc/dhcpd.conf, /etc/xinet.d/eb-xinetd, ~/eb (for event builder0), /etc/exports
2. Install SL6 64bit on the new ROPC
- Disable firewall (# /usr/bin/system-config-firewall-tui) and set Selinux permissive (# setenforce 1)
3. Extract the files
  [new ROPC : /] $ tar xvf tftpboot.tar
  And copy other files. ( /etc/dhcpd.conf should be placed under /etc/dhcp/ )
  (Re)start services; /sbin/service dhcpd(nfs,xinetd) restart, /sbin/chkconfig tftpboot on
4. Turn on COPPERs and see what happen.
[new ROPC: ] # tail –f /var/log/messages

## Slide 3: 2. Compiling DAQ program
Install basf2 on ROPC
  See https://confluence.desy.de/display/BI/Software+SoftwareInstallation
  Compile basf2 by ‘scons’ on ROPC
Compile DAQ programs
  ROPC : cd ~/basf2/release/daq/ropc; make ropc
  COPPER: cd ~/basf2/release/daq/ropc; make copper

## Slide 4: 3. Run DAQ program
Alternative scheme w/o eb0
Readout PC
recorder:
RecvStream1.py
RootOutput.root
Orange color components are basf2 components.
reader:
ReadStoreTemplate.py
Receive/send:
des_ser_ROPC_main
Receive data from HSLB and send to ROPC :
des_ser_COPPER_main
COPPER CPU
Receive data from HSLB and send to ROPC :
des_ser_COPPER_main
Receive/send:
des_ser_ROPC_main
COPPER CPU
[ropc:]$ ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/run_start_mono.sh

## Slide 5: 3, How to set parameters in scripts
Please see “Take data using COPPER and setting for that” at https://confluence.desy.de/display/BI/DAQ+PocketDAQ
  P.8 : How to modify daq/rawdata/example/RecvStream1.py
  P.14 and p.16 : How to modify daq/copper/daq_scripts/run_start_mono.sh