## Slide 1: Pocket DAQ manual (2014.7.19) rev.11654
Satoru Yamada

## Slide 2
COPPER
HSLB
HSLB
HSLB
HSLB
COPPER
CPU
Network
switch
Readout
PC (PXE boot server)
FEE
FEE
FEE
FEE
Ethernet
B2link
Connection between components
TTRX

## Slide 3
COPPER CPU
Readout PC
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
Merger :
eb0.cc
recorder:
RecvStream1.py
Software components
RootOutput.root
Orange color components are basf2 components.
reader:
RecvStore.py
These are stored under https://belle2.cc.kek.jp/svn/trunk/software/daq

## Slide 4: Pocket DAQ w/o slow controller and GUI

## Slide 5: 0. Before using pocket DAQ
Setup a PXE boot server for COPPER CPU and install driver for COPPER etc
  See https://belle2.cc.kek.jp/~twiki/bin/view/Detector/DAQ/PocketDAQ
Install basf2 on both COPPER CPU and Readout PC
  See https://belle2.cc.kek.jp/~twiki/bin/view/Software/SoftwareInstallation .
  “addall” does no install the daq package. You need to do “addpkg daq”.
  Check daq/Sconscripts and check if env['CONTINUE'] = False is commented out.
  Compile with scons.
Compile eventbuilder
  cd ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0/ ; gmake eb0

## Slide 6: Install GLEW for running basf2 program
After external ver.0.5.0?, basf2 requires GLEW(The OpenGL Extension Wrangler Library).
The following procedure worked fine.
1, install the yum epel repository.
ropc01$ wget http://ftp-srv2.kddilabs.jp/Linux/distributions/fedora/epel/5/i386/epel-release-5-4.noarch.rpm
ropc01$ ssh cpr** -lroot
cpr**# rpm -ivh epel-release-5-4.noarch.rpm
cpr**# ls -lrt /etc/yum.repos.d/
cpr**# exit
2, install glew on COPPER
ropc01$ sudo yum install glew --installroot=/tftpboot/copper/root

## Slide 7: 1, Set parameters(1)
[ROPC] % cd ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts
[ROPC] % emacs run_start.sh
Set arguments of start_copper.sh
Usage : start_copper.sh <HOSTNAME> <COPPER node ID> <FINNESSE bit flag: A=1, B=2, C=4, D=8> <Use network shared memory : Yes=1, No=0> <node name>
e.g.)
/usr/bin/xterm -fn 7x14 -geometry 102x10+0+642 -e ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/start_copper.sh cpr006 1 1 0 0&
/usr/bin/xterm -fn 7x14 -geometry 102x10+750+642 -e ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/start_copper.sh cpr007 2 3 0 0&
<COPPER node ID> will be attached to RawCOPPER header.

## Slide 8
1, Set parameters(2)
NOTICE : Environment variables for basf2
In ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/copper.sh, a line, “source ~/.bash_profile”, is for setting up basf2 environment. You need to add basf2 setting commands in your .bash_profile (or other script file).
Please see "Setup of Software Tools" at https://belle2.cc.kek.jp/~twiki/bin/view/Software/SoftwareInstallation for details.
[ ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/copper.sh ]
#
# setup basf2 environment (See "Setup of Software Tools" at https://belle2.cc.kek.jp/~twiki/bin/view/Computing/SoftwareInstallation
#
source ~/.bash_profile

## Slide 9
1, Set parameters(3)
Specify whether communication with GUI via shared memory will be used or not :
1, Edit ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/RecvStream1.py
If you use GUI, set ‘UseShmFlag’ = 1
receiver.param('UseShmFlag', 1)
If you don’t use GUI set ‘UseShmFlag’ = 0
receiver.param('UseShmFlag', 0)
2, Edit ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/RecvStream1.py
If you use GUI, set ‘UseShmFlag’ = 1
receiver.param('UseShmFlag', 1)
If you don’t use GUI set ‘UseShmFlag’ = 0
receiver.param('UseShmFlag', 0)

## Slide 10
2, Setting of merger (eb0) (1)
1, compile
$ cd ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0
$ make
2, edit eb0.sh
cd /home/usr/b2daq/eb # change to cd “your local BelleII directroy”/daq/eventbuilder/evb0/eb-xinetd
( e.g. cd /home/usr/yamada/basf2/release/daq/eventbuilder/evb0/eb-xinetd )
If you wan to read data from COPPERs with hostnames of cpr010, cpr011 and cpr012, use the following
./eb0 cpr010:33000 cpr011:33000 cpr012:33000

## Slide 11
2, Setting of merger (eb0) (2)
3, edit eb0’s part in ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0/eb-xinted
Modify user and server.
service eb0
{ bind = 127.0.0.1
socket_type = stream
type = UNLISTED
port = 5101
wait = no
user = g0cdc # Change to your user name (e.g. yamagata)
server = /home/usr/b2daq/eb/eb0.sh
# change to “your Belle2 local directory”/daq/eventbuilder/evb0/eb0.sh
# (e.g. /home/usr/yamagata/basf2/release/daq/eventbuilder/evb0/eb0.sh)
}
You need to change the other services in eb-xinetd ( eb1tx, eb1rx, eb2tx, eb2rx …. ) in the same way.

## Slide 12
4, Set link to eb-xinetd
# cd /etc/xinetd.d/
# ln –s ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0/eb-xinetd eb-xinetd
# /sbin/service xinetd restart
The eb0 daemon will be automatically invoked when a basf2 program on a readout PC connects to a port specified in eb-xinted.
2, Setting of merger (eb0) (3)

## Slide 13: 3, How to start DAQ
[ROPC] % cd ${BELLE2_LOCAL_DIR}/release/daq/copper/daq_scripts
[ROPC] % ./run_start.sh

## Slide 14: 4, How to stop DAQ
No stop button for now (If you use GUI, you have.)
You need to specify max # of events or time to stop the run on a basf2 python file.
ROPC % cd ${BELLE2_LOCAL_DIR}/daq/rawdata/examples
Edit RecvStream1.py
You can set following paramters to stop a run.
receiver.param('MaxTime', 300.)
receiver.param('MaxEventNum', 30.)
-1 means inifinite.

## Slide 15: 5. Read an output file and extract FEE buffer
Output file name
  ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/root_output.root
  You can change the filename by editing ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/RecvStream1.py
Read the root file
  Please see dataformat and unpacker manuals.
  Data format
    https://belle2.cc.kek.jp/svn/trunk/software/daq/copper/doc/SetupPocketDAQ_4p1_RawCOPPERDataHandling.pdf
  Unpacker
    https://belle2.cc.kek.jp/svn/trunk/software/daq/copper/doc/SetupPocketDAQ_4p5_RawDataUnpackerPacker.pdf

## Slide 16: End

## Slide 17: Revision history
2013/10/16
  Change explanation about option of run_start.sh script
2014/7/15 (rev. 11619)
  To specify FINESSE bit field, you need to use decimal value ( not hexadecimal ).
  Add an argument of RecvSenDCOPPER.py
  Update eb0 related issues.
    About eb0.sh
    About eb0-xinted
2014/7/16(rev. 11654)
  eb0.sh and eb-xinetd need more modification
2014/7/19
  Add a comment about “addpkg daq”

## Slide 18
Read Out PC
CDC test board
(Ver.3)
COPPER
FTSW
TTD
GbE
Belle2link
Clock+
Trigger
Test bench at Tsukuba B3