## Slide 1: RawData unpacker and packer
July 15, 2014 (SVN rev.11616)
Satoru Yamada

## Slide 2: 1, Unpacker

## Slide 3
You can get event # info from RawCOPPER object like this;
StoreArray<RawCOPPER> raw_cprarray; // When StoreArray is used
for (int i = 0; i < raw_cprarray.getEntries(); i++) { //When StoreArray is used
for ( int j = 0; j < raw_cprarray[ i ]->GetNumEntries(); j++) {
// Get Event number
unsigned int event_no = raw_cprarray[ i ]->GetEveNo( j );
// Get RawCOPPER data block
int* buf = raw_cprarray[ i ]->GetBuffer( j );
// See contents of a data block (from RawCOPPER header to RawCOPPER trailer)
for( int k = 0; k < raw_cprarray[ i ]->GetBlockNwords( j ); k++ ) printf("%.8x\n", buf[ k ] );
// Get Detector Buffer (raw data from detector electronics)
for( int finesse_num =0; finesse_num < 4; finesse_num++) {
int* buf_slot = raw_cprarray[ i ]->GetDetectorBuffer( j, finesse_num );
// See contents of raw data from detector
for( int k = 0; k < raw_cprarray[ i ]->GetDetectorNwords( j, finesse_num ); k++ ){
printf("%.8x\n", buf_slot[ k ] ); }
}
}
}
1-1, Example : how to get information of RawCOPPER header

## Slide 4: 1-2, Test program to read RawCOPPER(RawCDC) data
[INFO] Steering file: ReadStoreTemplate.py
>>> basf2 Python environment set
>>> Framework object created: fw
===== DataBlock(RawCDC) : Block # 0 : Event # 0 : node ID 0x00000000 : block size 224 bytes
== Detector Buffer(FINESSE A)
0x0094c13a 0x91000001
== Detector Buffer(FINESSE C)
0x0094c13a 0x91000001
===== DataBlock(RawCDC) : Block # 1 : Event # 1 : node ID 0x00000000 : block size 224 bytes
== Detector Buffer(FINESSE A)
0x0094c23f 0xf1000001
== Detector Buffer(FINESSE C)
0x0094c23f 0xf1000001
===== DataBlock(RawCDC) : Block # 2 : Event # 2 : node ID 0x00000000 : block size 224 bytes
== Detector Buffer(FINESSE A)
0x0094c30d 0x69000001
== Detector Buffer(FINESSE C)
0x0094c30d 0x69000001
….
1, Get dummy data file (data from two CDC FEE boards connected to FINESSE A and C.)
login.cc.kek.jp : ~yamadas/rawdata/root_output_RawCDC_rev7133.root
2, See contents of the data
% cd ${BELLE2_LOCAL_DIR}/daq/; svn update
% cd ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/
% basf2 ReadStoreTemplate.py -i ./root_output_RawCDC_rev7133.root | less
In this data,
Detector buffer contains only 2words(=8bytes)
per/FINESSE/event.
Note that block # is a number used by DAQ software
for handling data and not related with Event #.

## Slide 5
2, Packer

## Slide 6: 2-1, Function to store data in RawCOPPER object
Input variables :
int* detector_buf_*** : pointer to the detector buffer that you want to store as ***th FINESSE data.
int nwords_*** : length of the detector_buf_*** (unit -> word = 4bytes )
RawCOPPERPackerInfo rawcprpacker_info : Information to
fill RawHeader
void RawCOPPER::PackDetectorBuf( int* detector_buf_1st, int nwords_1st, int* detector_buf_2nd, int nwords_2nd, int* detector_buf_3rd, int nwords_3rd, int* detector_buf_4th, int nwords_4th, RawCOPPERPackerInfo rawcprpacker_info ){}
struct RawCOPPERPackerInfo {
unsigned int exp_num; // 10bit
unsigned int run_subrun_num; // 22bit
unsigned int eve_num; // 32bit
unsigned int node_id; // 32bit
unsigned int tt_ctime; // 27bit clock ticks at trigger timing distributed by FTSW. For details, see Nakao-san's belle2link user guide
unsigned int tt_utime; // 32bit unitx time at trigger timing distributed by FTSW. For details, see Nakao-san's belle2link user guide
unsigned int b2l_ctime; // 27bit clock ticks at trigger timing measured by HSLB on COPPER. For details, see Nakao-san's belle2link user guide
unsigned int hslb_crc16_error_bit; // 4bit errorflag for CRC errors in data transfer via b2link. ( bit0,1,2,3 -> finesse slot a,b,c,d)
unsigned int truncation_mask; // Not defined yet
unsigned int type_of_data; // Not defined yet
};
(#include <rawdata/include/RawCOPPERPackerInfo.h> )

## Slide 7
Module to fill dummy data in RawCOPPER
- rawdata/modules/src/DummyDataPacker.cc
Script to run the above module
- $ rawdata/scripts/DummyDataPacker.py
2-2, test program to store data in RawCOPPER object

## Slide 8: end

## Slide 9: Revision history
July 15, 2014 (rev.11616) : ver.1