## Slide 1: RawCOPPER data format
Aug. 27, 2015 (svn rev. 17269)
Satoru Yamada

## Slide 2
RawCOPPER header/trailer -> See Sec. 2
COPPER header/trailer -> See Sec.3
B2link(FEE+HSLB) header/trailer -> See Sec.4
Detector buffer -> Untouched by DAQ
1, Overview of RawCOPPER format (one data block from a COPPER board)

## Slide 3
COPPER
readoutPC
Binary
data
COPPER
readoutPC
PreRawCOPPER
format
PostRawCOPPER
format
HLT input server
Ropc disk
HLT input server
Ropc disk
Binary
data
RawCOPPER
format
RawCOPPER
format
RawCOPPER
format
RawCOPPER
format
PreRawCOPPER
format
PostRawCOPPER
format
1-1, Online header/trailer reduction
After
the update
PostRawCOPPER format : Ver # = 2
PreRawCOPPER format : Ver # = 2 + 0x80 = 129
Ver. # = 0
Ver. # = 0
Old Raw header/trailer
COPPER header/trailer
B2link header/trailer
Old Raw header/trailer
COPPER header/trailer
B2link header/trailer
New Raw header/trailer
COPPER header/trailer
B2link header/trailer
New Raw header/trailer
Reduced COPPER header/trailer
Reduced B2link header/trailer
Before rev. 11234
( June, 2014)
After rev. 11234
( June, 2014)

## Slide 4
• PreRawCOPPER format
• If you store data by COPPER CPU, then output data will be in Pre(reduction)RawCOPPER format.
• PostRawCOPPER format
• Store the data downstream from readout PC, the output data will be in Post(reduction)RawCOPPERFormat

## Slide 5
COPPER header (13words)
FINNESE A
RawCopper Header(20words)
COPPER trailer(3words?)
RawCopper Trailer(2words)
1 Number of total words
2 0x7f7f | Format ver.(8bit) | Number of words in this block ( 8bit )
3 exp no. (10bit=1024), run no.(22bit=4194304 including subrun )
4 event number(32bit)
From B2link FEE header 2 (TT-ctime | Trig-type)
From B2link FEE header 2 (TT-utime )
7 Node ID
8 b2link CRC error bit (4) | |truncation mask (truncated or not) / type of data
(compressed,calibration, …)
9 offset to 1st block of user’s data(FEE data)
10 offset to 2nd block of user’s data(FEE data)
11 offset to 3rd block of user’s data(FEE data)
offset to 4th block of user’s data(FEE data)
1 reserved (maybe used for checksum)
2 termination word of this block = 0x7fff0006
Detector buffer(slot A)
FINNESE A
Detector buffer(slot B)
FINNESE A
Detector buffer(slot C)
B2link(FEE/HSLB)
header
and
trailer
FINNESE A
Detector buffer(slot D)
Use this version number to distinguish
Different data format.
Ver.0 : to 2014. June(including DESY test)
ver.1 : from June.2014
Ver.2 : from Apr. 2015 (rev.17269)
2-1, “RawCOPPER header/trailer” format in PreRawCOPPER format (ver. 2+0x80)
* Same as ver.1

## Slide 6
2-2, “RawCOPPER header” and trailer format in PostRawCOPPER format (ver.0x02)
Same as PreRawCOPPER format
* Same as ver.1

## Slide 7
2-3, tentative format of 32bit node ID
(31-24) Detector ID : 8bit=256 : detector ID
(9-0) lower bits of COPPER ID : 10bit (1024)
Node ID = “TTD ” = 0x54544420 and “FTSW” are reserved for VME CPU and FTSW now.
Except for TRG, full COPPER ID can be reconstructed by “( Detector ID >> 24 ) * 1000 + COPEPR ID(12bit) “
e.g. NodeID = 0x0600000a -> COPPER ID = cpr6010
NodeID = 0x0100000a -> COPPER ID = cpr1010
For TRG data, full COPPER ID can be reconstructed by “ 9000 + COPEPR ID(12bit) “
  Following a request from SLC part, hostname of TRG coppers will be assigned as follows: (Aug.27, 2015)
CDC TRG : cpr1100*
ECL TRG : cpr1200*
…
GDLTRG : cpr1500*
A label of COPPER ID will be attached on the front of a COPPER board
Format :
Detector ID :
Full COPPER ID :
Detector ID (Defined in rawdata/dataobjects/include/RawCOPPERFormat.h)
• #define SVD_ID 0x01000000 // tentative
• #define CDC_ID 0x02000000 // tentative
• #define BPID_ID 0x03000000 // tentative
• #define EPID_ID 0x04000000 // tentative
• #define BECL_ID 0x05000000 // tentative
• #define EECL_ID 0x06000000 // tentative
• #define BKLM_ID 0x07000000 // tentative
• #define EKLM_ID 0x08000000 // tentative
#define TRGDATA_ID 0x10000000 // tentative
  #define CDCTRGDATA_ID 0x11000000 // tentative
  #define ECLTRGDATA_ID 0x12000000 // tentative
  #define TOPTRGDATA_ID 0x13000000 // tentative
  #define KLMTRGDATA_ID 0x14000000 // tentative
  #define GDLTRGDATA_ID 0x15000000 // tentative

## Slide 8
* Same as ver.1
2

## Slide 9
3-2, COPPER header and trailer in PostRawCOPPER format (ver. 0x02 )
No COPEPR header and trailer in Post reduction rawcopper format.
* Same as ver.1

## Slide 10
4-1, B2link FEE header/Trailer, B2link HSLB header/Trailer in
PreRawCOPPERFormat (ver. 0x02 + 0x80)
From Nakao-san’s Belle2link User guide (June 10, 2014):
You can download from 18 th B2GM indico page
http://kds.kek.jp/getFile.py/access?contribId=132&sessionId=28&resId=0&materialId=0&confId=15329
NOTICE :
To produce this format, the b2tt core used in
the FEE firmware should be the latest.
Please see Nakao-san’s following e-mails :
[b2link_ml:0143] Belle2link version 0.01 -
SVN update
And
[b2link_ml:0144] Re: Belle2link version 0.01 -
SVN update .
* Same as ver.1

## Slide 11
4-2, B2link FEE header/Trailer, B2link HSLB header/Trailer in
PostRawCOPPERFormat (ver. 0x02)
* Modified from ver.1
CRC error count(16)

## Slide 12
4-3, Older B2link header/trailer formats
At DESY test in January of 2014
From Nakao-san’s B2GM slides:
http://kds.kek.jp/getFile.py/access?contribId=143&sessionId=38&resId=0&materialId=slides&confId=13911

## Slide 13: 5-1, RawDataBlock object ( to handle Raw data from COPPER board )
RawDataBlock
RawCOPPER
RawFTSW
RawSVD
RawCDC
Raw…
RawDataBlock{
methods to access data;
int m_num_nodes; // # of nodes
int m_num_events;// # of events
int* m_buffer; -> buffer for data
}
Event # = n
Data From COPPER k1
Event # = n
Data From COPPER k2
Event # = n
Data From COPPER k3
Event # = n
Data From FTSW
Event # = n + 1
Data From COPPER k1
Event # = n + 1
Data From COPPER k2
Event # = n + 1
Data From COPPER k3
Event # = n + 1
Data From FTSW
Event n
Event (n+1)
In this example,
M_num_nodes = 4
M_num_events = 2.
# of data blocks = 4 * 2 = 8
m_buffer
Source code :
https://belle2.cc.kek.jp/svn/trunk/software/rawdata/dataobjects/
Example of data structure

## Slide 14
RecvSendCOPPER.py
DeSerializerCOPPER.cc
Event()
Serializer.cc
Event()
// Read 50 evens per an event() loop
For( int I =0; i< NUM_EVT_PER_BASF2LOOP_COPPER(=50);i++){
…
Num_event = 1; num_nodes = 1;
temp_rawdblk = raw_dblkarray.appendNew();
temp_rawdblk->SetBuffer(temp_buf, m_size_word, delete_flag, num_events, num_nodes)
…
}
// Send each raw_dblkarray[i] event
separately.
For( int I =0; i< raw_dblkarray.getEntries();i++){
…
sendByWriteV( raw_dblkarray[ I ])
…
}
Raw_dblkarray.getEntries()=50
Raw_dblkarray->GetNumNodes()=1
Raw_dblkarray->GetNumEvents()=1
Example of Data handling on COPPER (as of rev.12453)
Raw_dblkarray.getEntries()=50
Raw_dblkarray->GetNumNodes()=1
Raw_dblkarray->GetNumEvents()=1
Dump a ROOT file
Send data
to a readout
PC
From
FEE

## Slide 15
RecvSendCOPPER.py
DeserializerPC.cc
Event()
Serializer.cc
Event()
// Read 1 evens per an event() loop
For( int I =0; i< NUM_EVT_PER_BASF2LOOP_PC (=1);i++){
…
raw_datablkarray.appendNew();
…
}
For( int I =0; i< raw_dblkarray.getEntries();i++){
…
sendByWriteV( raw_dblkarray[ I ])
…
}
Raw_dblkarray.getEntries()=1
Raw_dblkarray->GetNumNodes()= # of COPPERs
Raw_dblkarray->GetNumEvents()=1
Raw_dblkarray.getEntries()=1
Raw_dblkarray->GetNumNodes()=# of COPPERs
Raw_dblkarray->GetNumEvents()=1
Dump a ROOT file
Send data
to eb1tx
(sender
daemon)
Example of Data handling on a readout PC (as of rev.12453)
COPPER
COPPER
COPPER
…
Eb0(partial event building daemon)

## Slide 16: Example : # of events and nodes in one RawDataBock(Detector) object and StoreArray :
test bench (PocketDAQ)
storage
COPPER A
RawDataBlock
Eve 0 : node A
RawDataBlock
Eve 0 : node B
Readout PC
Event builder (eb0)
StoreArray<RawDataBlock>
raw_datablockarray;
DeserializerPC.cc
raw_datablockarray[0];
# of event = 1, # of nodes = 2
HLT input server
COPPER B
Belle II
Storage
Raw2DsModule.cc
StoreArray<RawSVD>
raw_svdarray;
SVD
SVD
RawSVD
Eve 0: node A
RawSVD
Eve 0 : node B
raw_svdarray[0];
# of event = 1, # of nodes = 1
…
RawDataBlock
eve NUM_EVT-1 node A
raw_datablockarray[NUM_EVT-1];
# of event = 1, # of nodes = 2
NUM_EVT -> 50 on COPPER(DeserializerCOPPER.cc)
1 on a readoutPC(DeserializerPC.cc)
RawDataBlock
eve NUM_EVT -1
node B
raw_svdarray[1];
# of event = 1, # of nodes = 1
HLT, eb2
Ethernet
Ethernet
StoreArray structure of stored data
may be different.

## Slide 17: Example : how to store rawdata in RawDetector object by DAQ program
Full Belle II DAQ
  HLT(High Levele Trigger) receives serialized binary data from readout PCs and stores them in RawDetector Class. This RawDetector objects will be stored in storage.
    Module : daq/rfarm/event/modules/src/Raw2DsModule.cc
Pocket DAQ
  DATA are stored as a RawDataBlock object
  Example program can be used to convert RawDataBlock/COPPER to RawDetector objects
    Module : daq/rawdata/modules/src/Convert2RawDet.cc

## Slide 18: New RawCOPPER class
No change in style of the member functions -> No effect on derived class
Does not have a format information in itself
  Format class contains format information
    RawCOPPERformat.cc -> the latest format
      RawHeader.cc
    RawCOPPERformat_v0.cc -> an old format
      RawHeader_v0.cc
  Assgin a format class to m_access in CheckVersionSetBuffer()
  Use m_access to access buffer contents
inline int RawCOPPER::GetExpNo(int n)
{
CheckVersionSetBuffer();
return m_access->GetExpNo(n);
}
inline int RawCOPPER::GetRunNo(int n)
{
CheckVersionSetBuffer();
return m_access->GetRunNo(n);
}
2-2, Rawdata Unpacker for new and old data formats
Data taken at the DESY beam test(old format) can be read with the latest rawdata package
-> by checking data ver. In header.
Notice :
• RawCOPPER class supports both formats for
a while (0.5-1 year after the format becomes
stable?).
• In that case, the latest RawCOPPER
class cannot be used to read old format
• Of course, you can use old rawdata
repository to read old format
• For ver.0 format, use rawdata
repository before 11228

## Slide 20: Revision History of this document(1)
  • Jan.5, 2014 rev. 8376 : Add definition of tentative subsysID format
  • Dec. 16, 2013 rev.7974 :
  • Add B2linkFEE header format
  • Add comments about handling StoreArray when unpacking Raw*** data.
  • Oct.21, 2013 :rev.7133
  • Add instruction about Rawdata unpacking program
  • Oct. 18, 2013 :rev. 7095
  • 1 st draft
  • Jun. 23, 2014 : rev. 11234
  • Online (header/trailer) reduction scheme on readout PC is introduced
  • RawHeader format is changed
  • COPPER header/trailer format is changed
  • Nakao-san updated B2LFEE/HSLB header/trailer format
  • See [b2link_ml:0144] Re: Belle2link version 0.01 - SVN update
  Aug. 23, 2014: rev. 12453
    Add a description of how RawDataBLock objects are handled by the actual DAQ program.
  Sep. 26, 2014 : rev.13065
    Add TRG ID definition (0x09000000)
  Oct. 24, 2014 : rev. 13460
    Add a slide about # of events and nodes in one RawDataBock(Detector) object and StoreArray
    and how to store raw data in RawDetector object by DAQ program (p.16. p.17)
  Jan. 23, 2015: rev. 15030
    Modify TRGDATA_ID and add ***TRGDATA_ID for trigger from sub-detectors
  Mar.3, 2015 : rev. 15988
    Use “node ID” instead of subsystem ID.

## Slide 21: Revision History of this document(2)
  • Apr. 21, 2015 rev. 17269 : Description about a new data format (ver.2 )
  • Aug. 27, 2015 : Hostname of TRG COPPER are revised.

## Slide 22: Backup

## Slide 23
4-2, B2link FEE header/Trailer, B2link HSLB header/Trailer in
PostRawCOPPERFormat (ver. 0x01)
Modified part of data-format in the change from ver.1 to ver.2