## Slide 1: RawData unpacker and packer
Dec. 5, 2014 (SVN rev. 14322)
Satoru Yamada

## Slide 2: 1, Unpacker

## Slide 3
You can get event # info from RawCOPPER object like this;
StoreArray<RawCOPPER> raw_cprarray; // When StoreArray is used
for (int i = 0; i < raw_cprarray.getEntries(); i++) { //When StoreArray is used
for ( int j = 0; j < raw_cprarray[ i ]->GetNumEntries(); j++) {
// Get Event number
unsigned int event_no = raw_cprarray[ i ]->GetEveNo( j );
// Get RawCOPPER data block
int* buf = raw_cprarray[ i ]->GetBuffer( j );
// See contents of a data block (from RawCOPPER header to RawCOPPER trailer)
for( int k = 0; k < raw_cprarray[ i ]->GetBlockNwords( j ); k++ ) printf("%.8x\n", buf[ k ] );
// Get Detector Buffer (raw data from detector electronics)
for( int finesse_num =0; finesse_num < 4; finesse_num++) {
int* buf_slot = raw_cprarray[ i ]->GetDetectorBuffer( j, finesse_num );
// See contents of raw data from detector
for( int k = 0; k < raw_cprarray[ i ]->GetDetectorNwords( j, finesse_num ); k++ ){
printf("%.8x\n", buf_slot[ k ] ); }
}
}
}
1-1, Example : how to get information of RawCOPPER header

## Slide 4: 1-2, Test program to read RawCOPPER(RawCDC) data
[INFO] Steering file: ReadStoreTemplate.py
>>> basf2 Python environment set
>>> Framework object created: fw
===== DataBlock(RawCDC) : Block # 0 : Event # 0 : node ID 0x00000000 : block size 224 bytes
== Detector Buffer(FINESSE A)
0x0094c13a 0x91000001
== Detector Buffer(FINESSE C)
0x0094c13a 0x91000001
===== DataBlock(RawCDC) : Block # 1 : Event # 1 : node ID 0x00000000 : block size 224 bytes
== Detector Buffer(FINESSE A)
0x0094c23f 0xf1000001
== Detector Buffer(FINESSE C)
0x0094c23f 0xf1000001
===== DataBlock(RawCDC) : Block # 2 : Event # 2 : node ID 0x00000000 : block size 224 bytes
== Detector Buffer(FINESSE A)
0x0094c30d 0x69000001
== Detector Buffer(FINESSE C)
0x0094c30d 0x69000001
….
1, Get dummy data file (data from two CDC FEE boards connected to FINESSE A and C.)
login.cc.kek.jp : ~yamadas/rawdata/root_output_RawCDC_rev7133.root
2, See contents of the data
% cd ${BELLE2_LOCAL_DIR}/daq/; svn update
% cd ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/
% basf2 ReadStoreTemplate.py -i ./root_output_RawCDC_rev7133.root | less
In this data,
Detector buffer contains only 2words(=8bytes)
per/FINESSE/event.
Note that block # is a number used by DAQ software
for handling data and not related with Event #.

## Slide 5: 1-3, How to assign a buffer to RawDataBlock, RawCOPPER, RawSVD…
int* buffer = new int[nwords]; // data
RawCOPPER raw_copper;
Int delete_flag = 1; // if 1, raw_copper’s destructor will call “delete buffer;”
Int num_event = 1, num_nodes = 1; // If the buffer contains only 1 data block (usually so).
raw_copper.SetBuffer(buffer, nwords, delete_flag, num_event, num_nodes);
// When you want to convert a Raw*** type
{
RawSVD raw_svd;
delete_flag = 0; // in this case, raw_copper will delete buffer. So delete_flag=1 may cause double-free.
raw_svd.SetBuffer( raw_copper.GetWholeBuffer(), nwords, delete_flag, num_event, num_nodes);
RawDataBlock raw_datablock;
delete_flag = 0; // in this case, raw_copper will delete buffer. So delete_flag=1 may cause double-free.
raw_datablock.SetBuffer( raw_copper.GetWholeBuffer(), nwords, delete_flag, num_event, num_nodes);
}

## Slide 6
2, Packer

## Slide 7: 2-1, Function to store data in RawSVD(or other RawDetector ) object
Input variables :
int* detector_buf_*** : pointer to the detector buffer that you want to store as ***th FINESSE data.
int nwords_*** : length of the detector_buf_*** (unit -> word = 4bytes )
RawCOPPERPackerInfo rawcprpacker_info : Information to
fill RawHeader
void RawCOPPER::PackDetectorBuf( int* detector_buf_1st, int nwords_1st, int* detector_buf_2nd, int nwords_2nd, int* detector_buf_3rd, int nwords_3rd, int* detector_buf_4th, int nwords_4th, RawCOPPERPackerInfo rawcprpacker_info ){}
struct RawCOPPERPackerInfo {
unsigned int exp_num; // 10bit
unsigned int run_subrun_num; // 22bit
unsigned int eve_num; // 32bit
unsigned int node_id; // 32bit
unsigned int tt_ctime; // 27bit clock ticks at trigger timing distributed by FTSW. For details, see Nakao-san's belle2link user guide
unsigned int tt_utime; // 32bit unitx time at trigger timing distributed by FTSW. For details, see Nakao-san's belle2link user guide
unsigned int b2l_ctime; // 27bit clock ticks at trigger timing measured by HSLB on COPPER. For details, see Nakao-san's belle2link user guide
unsigned int hslb_crc16_error_bit; // 4bit errorflag for CRC errors in data transfer via b2link. ( bit0,1,2,3 -> finesse slot a,b,c,d)
unsigned int truncation_mask; // Not defined yet
unsigned int type_of_data; // Not defined yet
};
(#include <rawdata/include/RawCOPPERPackerInfo.h> )

## Slide 8
Module to fill dummy data in RawSVD
- rawdata/modules/src/DummyDataPacker.cc
Script to run the above module
- $ rawdata/scripts/DummyDataPacker.py
2-2, test program to store data in RawSVD(or other RawDetector ) object

## Slide 9: Example of packed data
===== DataBlock(RawSVD) : Block # 38
: Event # 3 : node ID 0x0100040e : block size 168 bytes
0000002a 7f7f010c 00400002 00000003 71234560 f1234567 0100040e 00000000 0000000c 00000012
00000019 00000021 ffaa0003 16543210 00000000 00000001 00000002 00030000 ffaa0003 16543210
00000001 00000002 00000003 00000004 00030000 ffaa0003 16543210 00000002 00000003 00000004
00000005 00000006 00030000 ffaa0003 16543210 00000003 00000004 00000005 00000006 00030000
00000000 7fff0006
===== FINESSE Buffer(FINESSE A) 0x3 words
ffaa0003 16543210 00000000 00000001 00000002 00030000
===== Detector Buffer(FINESSE A) 0x3 words
00000000 00000001 00000002
===== FINESSE Buffer(FINESSE B) 0x3 words
ffaa0003 16543210 00000001 00000002 00000003 00000004 00030000
===== Detector Buffer(FINESSE B) 0x4 words
00000001 00000002 00000003 00000004
===== FINESSE Buffer(FINESSE C) 0x3 words
ffaa0003 16543210 00000002 00000003 00000004 00000005 00000006 00030000
===== Detector Buffer(FINESSE C) 0x5 words
00000002 00000003 00000004 00000005 00000006
===== FINESSE Buffer(FINESSE D) 0x3 words
ffaa0003 16543210 00000003 00000004 00000005 00000006 00030000
===== Detector Buffer(FINESSE D) 0x4 words
00000003 00000004 00000005 00000006
Red : detector buffers

## Slide 10: end

## Slide 11: Revision history
July 15, 2014 (rev.11616) : ver.1
Aug. 8, 2014 (rev. 12158)
  Add instruction about setting a buffer to Raw*** object.
Dec. 5, 2014 (rev. 14322)
  Modify to produce multiple COPPER events
  Use RawSVD instead of RawCOPPER
  As a result, m_nodeid in DummyDataPacker.cc should be hard-coded.