## Slide 1: Information in EventMetaData and ‘Error event’
S. Yamada (KEK)
Jul. 1, 2016
1, Storing data in EventMetaData object by online DAQ
2, Definition of ‘Error event’ and how to avoid the event
2-1, Pocket DAQ case

## Slide 2
1, Storing data in EventMetaData object by online DAQ

## Slide 3
Red variables are supposed to be stored in EventMetadata by Raw2DsModule.cc of online DAQ program at an HLT input server. Currently m_time and m_production are not filled yet.
Rev. 28703 (framework/dataobjects/include/EventMetaData.h)
private:
unsigned int m_event; /**< Event number ('normal' data has values > 0). */
int m_run; /**< Run number (usually > 0, run-independent MC has run == 0). */
int m_subrun; /**< Sub-run number, increases indicate recovery from DAQ-internal trouble without change to detector constants. Not supposed to be used by offline analysis. */
int m_experiment; /**< Experiment number. (valid values: [0, 1023], run-independent MC has exp == 0) */
int m_production; /**< Unique identifier of the production of the event. */
unsigned long long int m_time; /**< Time in ns since epoch (1970-01-01). */
std::string m_parentLfn; /**< LFN of the parent file */
double m_generatedWeight; /**< Generated weight. */
unsigned int m_errorFlag; /**< Indicator of error conditions during data taking, ORed combination of EventErrorFlag values. */
Member variables of EventMetaData

## Slide 4
What daq/rfarm/event/modules/src/Raw2DsModule.cc is doing :
evtmetadata->setExperiment(sndhdr.GetExpNum()); // -> Added at rev. 8338
evtmetadata->setRun(sndhdr.GetRunNum()); // -> Added at rev. 8701
evtmetadata->setSubrun(sndhdr.GetSubRunNum()); // -> Added at rev. 28343
evtmetadata->setEvent(sndhdr.GetEventNumber()); // -> Added at rev. 8338
if (error_flag) evtmetadata->addErrorFlag(EventMetaData::c_B2LinkCRCError); // Added at rev.18569
Fill values in each variable as follows :
Pocket DAQ case :
There is no HLT input server and filling EventMetaData is done by DeSerializerPC.cc not Raw2DsModule.cc.
EventMetaData->getErrorFlag() can work if you use the DAQ program for data-taking after rev. 29676.

## Slide 5
2, Definition of ‘Error event’ and how to avoid the event

## Slide 6
‘Error event’ in this slides means that its EventMetaData.m_errorFlag is nonzero.
/** bit-flag format of m_error_flag */
enum EventErrorFlag {
c_B2LinkCRCError = 0x1, /**< Belle2link CRC error is detected in the event */
c_HLTError = 0x2 /**< Error is returned from HLT modules. */
};
In EventMetaData.h,
As of Jun. 2016, only c_B2LinkCRCError is implemented if using rev. 18569 or later.
Type of errors

## Slide 7
What is ‘m_errorFlag= c_B2LinkCRCError = 0x1’
Data-corruption during B2link data transfer is detected by CRC check.
-> m_errorFlag = 1
Data-corruption during B2link data transfer is not detected by CRC check.
-> m_errorFlag = 0
FEE
B2link
core
COPPER
ROPC
Calculate CRC value
and stores it.
ROPC re-calculates the CRC value
and compare it with the CRC value in a trailer.
If they don’t coincide, error bit in the RawCOPPER header(not EventMetaData) is set.
Later, the header is checked by Raw2DsModule on HLT and m_errorFlag is set to 1.
To HLT

## Slide 8
How to avoid CRC ‘error events’ :
call getErrorFlag() of EventMetaData:
event(){
…
if( EventMetaData->getErrorFlag() == 0 ){
// No CRC error
}else{
// CRC error event }
… }
For data taken with older DAQ program, you need to check each Raw*** object like the following; (*** is COPPER/SVD/CDC/TOP/ARICH/KLM )
StoreArray<Raw***> raw_ ***array;
for (int i = 0; i < raw_ *** array.getEntries(); i++) {
for (int k = 0; k < raw_ *** array[ i ]->GetNumEntries(); j++) {
if (raw_***array[ i ]->GetEventCRCError(k) != 0 ){
// CRC Error event !!
}
}
}
If the ver. of your DAQ program is old: (PocketDAQ before 29676, Belle2DAQ before rev. 18569 )
You need to check every Raw*** objects except for RawPXD.

## Slide 9: Test program to check error flag in EventMetaData in .(s)root files
$ cd ${BELLE2_LOCAL_DIR}/daq/rawdata/examples
$ basf2 CheckErrorEvent.py –i <.sroot file>
…
[INFO] Reading StreamerInfo
[INFO] SeqRootInput: initialized.
[INFO] CheckErrorEvent: initialize() started.
[INFO] CheckErrorEvent: initialize() done.
[INFO] SeqRootInput: beginRun called.
[INFO] Begin of new run
[INFO] Processed: 1 runs, 1 events
[INFO] Processed: 1 runs, 2 events
…
[INFO] Processed: 1 runs, 7000 events
[INFO] Seq File 1 closed
[INFO] SeqRootInput : 7984 events read with total bytes of 113506 kB
[INFO] SeqRootInput : event rate = 10.2758 (KHz)
[INFO] SeqRootInput : flow rate = 146.088 (MB/s)
[INFO] SeqRootInput : event size = 14.2167 +- 1.26828 (kB)
[INFO] SeqRootInput: endRun done.
Event CRC error 0 CPRs 0 Events (obtained by checking each Raw*** header)
Event CRC error 0 Events (obtained by checking EventMetaData. it should be equal to the above value. )
-> In this case, No CRC ‘error events’ stored in EventMetaData are detected.

## Slide 10: end