## Slide 1: Pocket DAQ manual (rev. 17080)
Apr. 15, 2015
Satoru Yamada

## Slide 2
COPPER II
HSLB
HSLB
HSLB
HSLB
COPPER
CPU
Network
switch
Readout
PC (PXE boot server)
FEE
FEE
FEE
FEE
Ethernet
B2link
Connection between components (COPPER-II)
TTRX ver.4
FTSW
VME CPU(VMIC)
About port assignment of FTSW, see
svn+ssh://xxx@bdaq.local.kek.jp/bdaq/svn/firmware/ft2u/trunk/doc/ft2u.pdf
Cat7 LAN cable
6U slots
9U slots

## Slide 3
COPPER III
HSLB
HSLB
HSLB
HSLB
COPPER
CPU
Network
switch
Readout
PC (PXE boot server)
FEE
FEE
FEE
FEE
Ethernet
B2link
Connection between components (COPPER-III)
TTRX ver.5
FTSW
VME CPU(VMIC)
About port assignment of FTSW, see
svn+ssh://xxx@bdaq.local.kek.jp/bdaq/svn/firmware/ft2u/trunk/doc/ft2u.pdf
Cat7 LAN cable
9U slots
6U slots

## Slide 4
COPPER CPU
Readout PC
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
Merger :
eb0.cc
recorder:
RecvStream1.py
Old Software components
RootOutput.root
Orange color components are basf2 components.
reader:
ReadStore.py
These are stored under https://belle2.cc.kek.jp/svn/trunk/software/daq
COPPER CPU
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py

## Slide 5
Readout PC
Merger :
eb0.cc
recorder:
RecvStream1.py
Old Software components (from rev. 13542 to rev. 15005)
RootOutput.root
Orange color components are basf2 components.
reader:
ReadStoreTemplate.py
These are stored under https://belle2.cc.kek.jp/svn/trunk/software/daq
recorder:
RecvStream0.py
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
COPPER CPU
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
recorder:
RecvStream0.py
COPPER CPU

## Slide 6
Readout PC
Merger :
eb0.cc
recorder:
RecvStream1.py
New Software components (from rev. 15006)
RootOutput.root
Orange color components are basf2 components.
reader:
ReadStoreTemplate.py
These are stored under https://belle2.cc.kek.jp/svn/trunk/software/daq
Receive/send:
RecvStream2.py
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
COPPER CPU
Receive data from HSLB and send to ROPC :
RecvSendCOPPER.py
Receive/send:
RecvStream2.py
COPPER CPU

## Slide 7: Pocket DAQ w/o slow controller and GUI

## Slide 8: 0. Before using pocket DAQ
Setup a PXE boot server for COPPER CPU and install driver for COPPER etc
  See https://belle2.cc.kek.jp/~twiki/bin/view/Detector/DAQ/PocketDAQ
Install basf2 on both COPPER CPU and Readout PC
  See https://belle2.cc.kek.jp/~twiki/bin/view/Software/SoftwareInstallation .
  “addall” does no install the daq package. You need to do “addpkg daq”.
  Check daq/Sconscripts and comment out “if env['CONTINUE'] = False” line.
  Compile with scons.
Compile eventbuilder
  cd ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0/ ; gmake eb0

## Slide 9: Notice from Konno-san about compiling daq package
Please run the following command to update nsm2 programs in your external directory
$ source ${BELLE2_LOCAL_DIR}/ daq/slc/extra/nsm2/export.sh
Otherwise you may get error messages about compilation of slow control programs ;
daq/slc/nsm/src/NSMData.cc: In member function 'void* Belle2::NSMData::parse(const char*, bool)':
daq/slc/nsm/src/NSMData.cc:299:68: error: too many arguments to function 'NSMparse* nsmlib_parsefile(const char*, int, const char*, char*)'
In file included from include/daq/slc/nsm/NSMData.h:20:0,
from daq/slc/nsm/src/NSMData.cc:1:
IMPORTANT!

## Slide 10: Install GLEW for running basf2 program
After external ver.0.5.0?, basf2 requires GLEW(The OpenGL Extension Wrangler Library).
The following procedure worked fine.
1, install the yum epel repository.
ropc01$ wget http://ftp-srv2.kddilabs.jp/Linux/distributions/fedora/epel/5/i386/epel-release-5-4.noarch.rpm
ropc01$ ssh cpr** -lroot
cpr**# rpm -ivh epel-release-5-4.noarch.rpm
cpr**# ls -lrt /etc/yum.repos.d/
cpr**# exit
2, install glew on COPPER
ropc01$ sudo yum install glew --installroot=/tftpboot/copper/root

## Slide 11: 0.5, Set active HSLB slots in TTRX register
From Nakao-san’s mail : [b2link_ml:0159] Re: ft2u-0.65, b2tt-0.31, hslb-0.36
To partially mask HSLB, one can modify register 130 of tt4r:
- setting each of bit 0..3 to 0 corresponds to masking HSLB A..D
- default value of register 130 is 0010000f (all HSLB are enabled)
- bit 20..23 are read only and should be 1 as above
- for example, one can mask HSLB-A by
copper_CPU $ regrx 130 0000000e
Example :
When you use;
Slot A : copper_CPU $ regrx 130 00000001
Slot B : copper_CPU $ regrx 130 00000002
Slot A and B : copper_CPU $ regrx 130 00000003

## Slide 12: 1, Set parameters in run_start.sh (1)
[ROPC] % cd ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts
[ROPC] % emacs run_start.sh
Set arguments of start_copper.sh
Usage : start_copper.sh <HOSTNAME> <COPPER node> <FINNESSE bit flag: A=1, B=2, C=4, D=8> <Use network shared memory : Yes=1, No=0> <node name(used for Network Shared Memory)>
e.g.)
/usr/bin/xterm -e ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/start_copper.sh cpr006 1 1 0 0&
/usr/bin/xterm -e ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/start_copper.sh cpr007 2 3 0 0&
<COPPER node ID> will be attached to RawCOPPER header.

## Slide 13
1, Set parameters in run_start.sh (2)
NOTICE : Environment variables for basf2
In ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/copper.sh, a line, “source ~/.bash_profile”, is for setting up basf2 environment. You need to add basf2 setting commands in your .bash_profile (or other script file).
Please see "Setup of Software Tools" at https://belle2.cc.kek.jp/~twiki/bin/view/Software/SoftwareInstallation for details.
[ ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/copper.sh ]
#
# setup basf2 environment (See "Setup of Software Tools" at https://belle2.cc.kek.jp/~twiki/bin/view/Computing/SoftwareInstallation
#
source ~/.bash_profile

## Slide 14
1, Set parameters in run_start.sh (3)
Set arguments of RecvStream2.sh
Usage : RecvStream2.py <COPPER hostname> <Use NSM(Network Shared Memory)? yes=1/no=0> <port # to accept connection from eb0 > <NSM nodename>
Example :
/usr/bin/xterm -e "${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/RecvStream2.sh cpr001 0 34001 hogehoge1000;” &
/usr/bin/xterm -e "${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/RecvStream2.sh cpr007 0 34007 hogehoge1000;” &
Readout PC
Merger :
eb0.cc
RecvStream2.py
cpr001
cpr007
RecvStream2.py
Port
33000
Port
33000
Port
34001
Port
34007

## Slide 15
1, Set parameters in run_start.sh (4)
Specify whether communication with GUI via shared memory will be used or not :
1, Edit ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/RecvStream1.py
If you use GUI, set ‘UseShmFlag’ = 1
receiver.param('UseShmFlag', 1)
If you don’t use GUI set ‘UseShmFlag’ = 0
receiver.param('UseShmFlag', 0)
2, Edit ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/RecvStream2.py
If you use GUI, set ‘UseShmFlag’ = 1
receiver.param('UseShmFlag', 1)
If you don’t use GUI set ‘UseShmFlag’ = 0
receiver.param('UseShmFlag', 0)

## Slide 16
2, Setting of merger (eb0) (1)
1, compile
$ cd ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0
$ make
2, edit eb0.sh
cd /home/usr/b2daq/eb # change to cd “your local BelleII directroy”/daq/eventbuilder/evb0/eb-xinetd
( e.g. cd /home/usr/yamada/basf2/release/daq/eventbuilder/evb0/eb-xinetd )
If you want to read data from COPPERs with hostnames of cpr010, cpr011 and cpr012 and corresponding port # of RecvStream2.py are 34010, 34011 and 34012, respectively, use the following ;
./eb0 cpr010:33000 cpr011:33000 cpr012:33000
./eb0 localhost:34010 localhost:34011 localhost:34012
Merger :
eb0.sh
RecvStream2.py
cpr010
cpr011
RecvStream2.py
Port
33000
Port
33000
Port
34010
Port
34011
cpr012
RecvStream2.py
Port
33000
Port
34012
Readout PC (localhost)
RecvStream1.py

## Slide 17
2, Setting of merger (eb0) (2)
3, edit eb0’s part in ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0/eb-xinted
Modify user and server.
service eb0
{ bind = 127.0.0.1
socket_type = stream
type = UNLISTED
port = 5101
wait = no
user = g0cdc # Change to your user name (e.g. yamagata)
server = /home/usr/b2daq/eb/eb0.sh
# change to “your Belle2 local directory”/daq/eventbuilder/evb0/eb0.sh
# (e.g. /home/usr/yamagata/basf2/release/daq/eventbuilder/evb0/eb0.sh)
}
You need to change the other services in eb-xinetd ( eb1tx, eb1rx, eb2tx, eb2rx …. ) in the same way.

## Slide 18
4, Set link to eb-xinetd
# cd /etc/xinetd.d/
# ln –s ${BELLE2_LOCAL_DIR}/daq/eventbuilder/evb0/eb-xinetd eb-xinetd
# /sbin/service xinetd restart
The eb0 daemon will be automatically invoked when a basf2 program on a readout PC connects to a port specified in eb-xinted.
2, Setting of merger (eb0) (3)

## Slide 19: 3, How to start DAQ
[ROPC] % cd ${BELLE2_LOCAL_DIR}/release/daq/copper/daq_scripts
[ROPC] % ./run_start.sh
It is convenient to login COPPER w/o typing password.
For example;
ropc $ cd ~/.ssh
ropc S ssh-keygen rsa
ropc $ cat ./id_dsa.pub >> authorized_keys
ropc $ chmod 600 authorized_keys

## Slide 20: 4, How to stop DAQ
No stop button for now (If you use GUI, you have.)
You need to specify max # of events or time to stop the run on a basf2 python file.
ROPC % cd ${BELLE2_LOCAL_DIR}/daq/rawdata/examples
Edit RecvStream1.py
You can set following paramters to stop a run.
receiver.param('MaxTime', 300.)
receiver.param('MaxEventNum', 30.)
-1 means inifinite.

## Slide 21: 5. Read an output file and extract FEE buffer
Output file name
  ${BELLE2_LOCAL_DIR}/daq/copper/daq_scripts/root_output.root
  You can change the filename by editing ${BELLE2_LOCAL_DIR}/daq/rawdata/examples/RecvStream1.py
Read the root file
  Please see dataformat and unpacker manuals.
  Data format
    https://belle2.cc.kek.jp/svn/trunk/software/daq/copper/doc/SetupPocketDAQ_4p1_RawCOPPERDataHandling.pdf
  Unpacker
    https://belle2.cc.kek.jp/svn/trunk/software/daq/copper/doc/SetupPocketDAQ_4p5_RawDataUnpackerPacker.pdf

## Slide 22: Revision history(1)
2013/10/16
  Change explanation about option of run_start.sh script
2014/7/15 (rev. 11619)
  To specify FINESSE bit field, you need to use decimal value ( not hexadecimal ).
  Add an argument of RecvSenDCOPPER.py
  Update eb0 related issues.
    About eb0.sh
    About eb0-xinted
2014/7/16(rev. 11654)
  eb0.sh and eb-xinetd need more modification
2014/7/19
  Add a comment about “addpkg daq”
2014/8/8
  Modify usage of start_run.sh. (nodename is only used for NSM)
2014/10/29
  Change a DAQ scheme so that RecvStream0.py is used on a readout PC
2014/11/10
  Add figures to indicate connection between COPPER and FTSW
  Add procedure to ssh-login w/o typing password
2014/11/14
  Add “Notice from Konno-san about compiling daq” page
2015/1/22
  Use RecvStream2.py(=DesSerPrePC.cc) instead of RecvStream0.py(=DeSerializerPrePC.cc+Serializer.cc)

## Slide 23: Revision history(2)
2015 4/13
  Add “0.5, Set active HSLB slots in TTRX register”

## Slide 24: Appendix

## Slide 25: A-1, yum setting for COPPER
Sometime yum fails when you try to install software to COPPER directory;
readoutPC # yum install **** --installroot=/tftpboot/copper/root
In that case, you need to change yum setting for COPPER host:
1, Copy yum repository files. readoutPC # cp /etc/yum.repo.d/* /tftpboot/copper/root/etc/yum.repo.d/*
2, Set a proxy server in /tftpboot/copper/root/etc/yum.conf same as readoutPC:/etc/yum.conf

## Slide 26: A-2, Socket parameters on COPPER, readout PC and etc..
1, Enable “Jumbo Frame” in network switch’s setting, if necessary (e.g. HP1810-24G)
If the switch does not support Jumbo frame, setting MTU a large value may cause a problem.
2, Change socket parameters
# /sbin/ifconfig eth? mtu 9000
# /sbin/sysctl -w net.ipv4.tcp_rmem="8388608 8388608 8388608"
# /sbin/sysctl -w net.ipv4.tcp_wmem="8388608 8388608 8388608"
# /sbin/sysctl -w net.ipv4.tcp_mem="9000000 9000000 9000000"
# /sbin/sysctl -w net.core.rmem_default=8388608
# /sbin/sysctl -w net.core.wmem_default=8388608
# /sbin/sysctl -w net.core.rmem_max=8388608
# /sbin/sysctl -w net.core.wmem_max=8388608
3, edit /etc/rc.local(or /tftpboot/copper/root/etc/rc.local ) if you want the parameters automatically set at boot time

## Slide 27
A-3, Use ntpd to adjust time on COPPER
1, Edit /tftpboot/copper/root/etc/rc.d/init.d/ntpd
# Source networking configuration.
. /etc/sysconfig/network
ntpdate 192.168.10.1
if [ -f /etc/sysconfig/ntpd ];then
. /etc/sysconfig/ntpd
fi
2, check ntpd is started at boot time
cpr**** $ chkconfig –list | grep ntp

## Slide 28: A-4, syslogd
Install syslogd :
readoutPC # yum install syslogd --installroot=/tftpboot/copper/root
Add entry to /tftpboot/copper/root/etc/syslogd.conf if needed:
# Log anything (except mail) of level info or higher.
# Don't log private authentication messages!
*.info;mail.none;news.none;authpriv.none;cron.none /var/log/messages

## Slide 29
Read Out PC
CDC test board
(Ver.3)
COPPER
FTSW
TTD
GbE
Belle2link
Clock+
Trigger
B-1, Test bench at Tsukuba B3